## Slide 1: Lab 4 Fourier Transform

## Slide 2
Objective
From Fourier series to Fourier transform.
Analyze the signals with Fourier Transform.
Analyze the LTI system with system models.

## Slide 3
Relationship
The interval of spectrum line:
Main lobe width:
Amplitude:
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 4
The Influence of T
The interval of spectrum line:
Main lobe width:
Amplitude:
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 5
Fourier Series and Fourier Transform

## Slide 6
Fourier Transform and Inverse Fourier Transform
The Fourier transform of f(t):
The inverse Fourier transform:
Complex exponential Fourier series
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 7
Fourier Transform with Matlab
Fourier Transform
Numeric method
Symbolic method
Direct method
Function:fft
Signal Analyzer
Function:fourier/ifourier
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 8
Symbolic Method
Fourier transform:
  F = fourier(f)
  F = fourier(f,v)
  F = fourier(f,u,v)
Inverse Fourier transform:
  f = ifourier(F)
  f = ifourier(F,u)
  f = ifourier(F,v,u)
Use function abs and angle to plot the amplitude-frequency and phase-frequency
e.g.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 9
Numeric Method
Fourier transform:
  Y = fft(x)
  Y = fft(x,n)
Inverse Fourier transform
  x = ifft(Y)
  x = ifft(Y,n)
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 10
Numeric Method
x=
cos(2*pi*10.*t)+
2sin(2*pi*15.*t)+
3cos(2*pi*20.*t)
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 11
Numeric Method
x=cos(2*pi*10.*t)+2sin(2*pi*15.*t)+3cos(2*pi*20.*t)
N = 256;
Fs = 100;
t = [0:N-1]./Fs;
x=1*cos(2*pi*10.*t)+2*sin(2*pi*15.*t)+3*cos(2*pi*20.*t);
Y = fft(x,N);
plot(abs(Y))
Amplitude | Frequency
1 | 10
2 | 15
3 | 20
ts = 0.01; Fs = 1/ts
N = 256;
t = 0:ts: (N-1)*ts;
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 12
Numeric Method
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 13
Numeric Method
N = 256;
Fs = 100;
df = Fs/N;
f = [0:N-1]*df;
t = [0:N-1]./Fs;
x=1*cos(2*pi*10.*t)
+2*sin(2*pi*15.*t+deg2rad(30))
+3*cos(2*pi*20.*t+deg2rad(-30));
Y = fft(x);
Yabs = abs(X);
Yabs = 2*Yabs/N;
Yabs(1) = Yabs(1)/2;
Yabs = Yabs(1:N/2);
f = f(1:N/2);
plot(f,Yabs)
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 14
Numeric Method
Notices
  We only interested in the first half of the fft results.
  The corresponding frequency to the X(n) is calculated by , where is the frequency resolution.
  As mentioned in 1 and 2, the effective observation items are from 1th to th, so the corresponding frequency is from 0 to.
  To get the amplitude, the 1st and th item should be divided by N, and the others be divided by .
  According to the characters of function fft, it is recommend that N prefers. （nextpow2()）
  To avoid spectrum leak, the frequency of signal should be an integer multiple of the frequency resolution.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 15
Frequency Leakage
Both sampling and windowing produce frequency leakage.
fft may aggravate spectrum leakage.
  To reduce the spectrum leak, the frequency of signal should be an integer multiple of the frequency resolution:
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 16
Frequency Leakage
K=f*N/Fs, N=256 |  |  | 
 | f=10Hz, Amp=1 | f=15Hz, Amp=2 | f=20Hz, Amp=3
Fs=120Hz | k=21.33 | k=32 | k=42.7
Fs=160Hz | k=16 | k=24 | k=32
K=f*N/Fs, Fs=100Hz |  |  | 
 | f=10Hz, Amp=1 | f=15Hz, Amp=2 | f=20Hz, Amp=3
N=260 | k=26 | k=39 | k=52
N=250 | k=25 | k=37.5 | k=50
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 17
Periodic signals and aperiodic signals
FFT is an efficient DFT algorithm. It is an operation of discrete signals. The definition of DFT is:
When performing fft on a continuous signal, the continuous signal needs to be sampled fist.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 18
Periodic signals and aperiodic signals
For a continuous periodic signal x(t) with a period T0, its Fourier series is
  After sampling N points in T0:
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 19
Periodic signals and aperiodic signals
For a continuous aperiodic signal x(t), its Fourier transform is
  After sampling:
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 20
Direct Fourier Transform
Expressed in the matrix:
e.g.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 21
Signal Analyzer APP
APP->Signal Analyzer
e.g.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇

## Slide 22
System Analysis
e.g.
Notes: 谱线间隔：𝜔_1=2𝜋/𝑇_1
主瓣宽度：2𝜋/𝜏 𝐸𝜏/𝑇