## Slide 1: Implementing Collective Communication
CS121 Parallel Computing
Spring 2018

## Slide 2: Collective communication
Important as the basis for many parallel algorithms.
Implemented using multiple point to point communications, possibly in parallel.
  Assume communicating m words (without contention) between a source and destination takes ts + m tw time.
    Ignore the the distance of the message, since per hop latency th usually small.
  With contention c, time becomes ts + c m tw.
Implementations depend on communication hardware architecture.
Operations
  Broadcast and reduction.
  All-to-all broadcast and reduction.
  All-reduce, prefix sum.
  Scatter and gather.
  All-to-all scatter and reduce.
  Circular shift.

## Slide 3: Broadcast and reduction on ring
Source: Introduction to Parallel Computing, Grama et al
Start with root sending message to distance p/2 node.
In later stages all nodes with the message send it distance d/2, where d is distance of during last stage.
Reduction has reverse communication pattern.
Cost
With p processors, log p steps.
In each step, a processor sends a size m message.
  Total time (ts + m tw) log p.

## Slide 4: Broadcast on mesh
Root first broadcasts along its row using ring algorithm.
The nodes of root’s row then broadcast along their columns using ring algorithm.
Cost
log Öp = (log p) / 2 steps along row, same along columns.
  Total time (ts + m tw) log p.

## Slide 5: Broadcast on hypercube
All nodes with message send.
Send in parallel along the dimensions in order.
Again, log p steps, so total time (ts + m tw) log p.

## Slide 6: All-to-all broadcast on ring
For a size p ring, run in p-1 steps.
Keep passing data down the ring. Processes store any new data they receive.
Numbers in parentheses show the data a process has received by a certain time.
Cost is (ts + m tw) (p-1).

## Slide 7: All-to-all broadcast on mesh
First do all-to-all broadcast along each row using ring algorithm.
After this, each process has a Öp pieces of data.
Then do all-to-all broadcast along each column using ring algorithm.
  Each node sends data with size Öp.
Cost
First stage has Öp-1 steps and (ts + m tw) (Öp -1) cost.
Second stage has Öp-1 steps and (ts + m Öp tw) (Öp -1) cost because each message has mÖp size.
Total cost 2 ts (Öp -1) + m tw (p -1)

## Slide 8: All-to-all broadcast and reduce on hypercube
In each step, each process sends all the data it has received along a dimension.
log p steps total.
In step i, send messages of size 2i.
Total cost
All-to-all reduce has same communication pattern, except processes add all the data they receive.
So each message only has size m, and total cost is (ts + m Öp tw) log p.

## Slide 9: Prefix sum on hypercube
Each process keeps two values, its prefix sum p (shown in brackets), and the sum s of all the values it’s received (shown in parentheses).
  There are some mistakes in the s values, e.g. in figure (b) the (6) value should be (6+7), and in figure (c), (4+5+6) should be (4+5+6+7)
In each step, each process
  Sends its s value along a new dimension, in order of least to most significant dimension.
  Adds s it receives into its own s.
  If it received s from a lower ordered process, it adds the new s into its current p.
This works correctly because by the time a process is ready to receive data along a dimension, all values of processes in lower dimensions have been summed in s and will be sent.
There are log p steps, and the total cost is (ts + m tw) log p.

## Slide 10: Scatter and gather
Initially root has p pieces of data.
In each step, a process sends half the data it’s received along a new dimension.
Total cost
Gather reverses the communication, and has the same cost.

## Slide 11: All-to-all personalized on ring
Dotted lines shown different steps of communication.
p-1 steps for p processes.
Each process starts with p pieces of data.
Each time it receives data, it keeps the piece intended for it, and passes on the rest.
Cost

## Slide 12: All-to-all personalized on mesh
Each row first breaks its data into Öp blocks, each block containing all its messages for nodes within a different column.
Then it does all-to-all personalized with the blocks to its row.
Next, do all to all personalized along each column.
Each phase involves all-to-all personalized sending of data of size to processors.
Using previous equation, total cost is
.

## Slide 13: All-all personalized on hypercube
Send in order of dimension from least to most significant.
  For dimension i, send all data with destination differing in i’th least significant bit.
  Each step confines broadcast problem to one less dimension.
Total of log p steps, and send p/2 amount of data in each step.
Total time (ts + m p tw / 2) log p.
Each process receives m (p-1) pieces of data.
Average distance between processes (log p)/2.
Total communication volume m(p-1)(log p) / 2.
Number of links in hypercube is p log p / 2.
So lower bound on communication is volume divided by number of links, i.e. tw m (p-1).
This algorithm isn’t optimal.

## Slide 14: All-all personalized on hypercube
Another method for all-to-all personalized communication is for each process to send one message to each other process.
Run for p-1 steps. In step j, process i sends data to process (i XOR j).
  Message routed using E-cube routing (i.e. send in order of increasing dimension.)
  A hypercube is so well connected that this communication pattern can be routed with no congestion, assuming bidirectional links.
So each message sent in ts + m tw time, and total time is (ts + m tw) (p-1), which is optimal.

## Slide 15: Circular shift on mesh
Given a shift of k, process p sends to (p+k) mod p.
Do k mod Öp shifts along x dimension, ëk / Öpû shifts along y dimension.
First, shift along the x dimension.
For each x shift, need to do a compensatory shift in the first column.
  E.g. in figure (b), 3’s message should be at node 4, not 0.
Then shift along y dimension.
The movement in either dimension is at most Öp.
Each shift costs ts + m tw, so total cost (ts + m tw) (Öp+1).

## Slide 16: Circular shift on hypercube
To shift in hypercube, first map the ring into the hypercube using the Gray code construction.
  For any i > 0, any two nodes differing by 2i in ring are mapped to nodes distance 2 apart in the hypercube.
  Ex Nodes 2 and 6 get mapped to (011)2 and (101)2, resp.
  Neighbors in the ring are mapped to neighbors in the hypercube.
To shift by k, write k in binary, then shift along dimensions with 1 digits.
  Ex To shift by 5=(101)2, each node shifts along dimension 0, then 2.
  For each dimension , shifting by takes 2 steps.
  Shifting along dimension 0 takes 1 step.
Shift along at most log p dimensions, so cost is (ts + m tw) log p.